* * * DECTAPE UTILITY SYSTEM * * *
VERSION: 11      DATE:19-JAN-72

GENERAL DESCRIPTION
------- -----------
A.  THIS SYSTEM CONSISTS OF A DATA FILE AND AN OPERATOR CONTROL
   PROGRAM BOTH OF WHICH RESIDE ON THE DISK UFD [1,4].
     THE DATA FILE CALLED DTAPPN.SYS CONSISTS OF ONE ENTRY PER DECTAPE.
   AN ENTRY IS THE PROJECT-PROGRAMMER NUMBER PAIR (PPN) ASSOCIATED WITH
   THE DECTAPE IDENTIFICATION NUMBER (ID).  THE LOCATION OF THE ENTRY IS
   (ID) ON THE DATA FILE.

     THIS PROGRAM PERFORMS SEVERAL FUNCTIONS DESCRIBED
BELOW.  IT RETRIEVES THE PERSONAL NAME ASSOCIATED WITH THE
PPN FROM PASWRD.TXT LOCATED IN [1,4].  THIS PROGRAM IS RUN
UNDER A DECTAPE PRIVILEGED JOB.

B.   GIVE COMMANDS AND THEIR FUNCTIONS
     INFORMATION COMMANDS
     1. H - PRINT THE COMMANDS FEATURED IN THIS PROGRAM.
     2. P - PRINT WILL ACCEPT EITHER OF TWO TYPES OF ARGUMENTS.
	A) PRINT IDM,IDN - PRINT THE PPN
	   ASSOCIATED WITH ALL DECTAPES FROM IDM TO IDN.
	   (SINGLE ID ALSO ACCEPTABLE AS ARGUMENT).
	B) PRINT [PJ,PG] - PRINT ALL DECTAPES WITH THIS PPN.
	   (] IS OPTIONAL TERMINATOR).
     3. L - LIST ON THE LINE PRINTER THE ID, THE ASSOCIATED
        PPN, AND THE PERSONAL NAME OF ALL DECTAPES.  ALSO LIST
        A CROSS REFERENCE OF ALL PPN'S AND THEIR ASSOCIATED DECTAPES.
     4. T - SAME AS L ONLY LIST ON THE TELETYPE.
     ACTION COMMANDS
     5. C - CHANGE THE ID AND-OR PPN.
        THE ID NUMBER IS INSERTED INTO THE LAST WORD OF BLOCK 100
        AND THE PPN ENTERED ON DTAPPN.SYS AT (ID).  IF NO PPN IS 
        SPECIFIED, THE ID IS INSERTED.
     6.  S ID - CLEAR THE DECTAPE DIRECTORY AND THE ENTRY (ID)
        FROM DTAPPN.SYS. THE ID NUMBER IS PERSERVED.
     7. U - UNWIND AND UNLOAD THE DECTAPE.


INPUT SPECIFICATION
----- -------------
1. TELETYPE - GIVE ACCEPTS ONE CHARACTER COMMANDS FROM THE
   TELETYPE. ALSO,SERIAL NIMBERS AND PPN MAY BE SPECIFIED.
2. DISK - A FILE DTAPPN.SYS IS KEPT ON THE DISK AREA[1,4]. DTAPPN.SYS
   CONSISTS OF ONE ENTRY PER DECTAPE. THE NTH ENTRY CONTAINS THE PPN
   ASSOCIATED WITH DECTAPE NUMBER N. IF THE DECTAPE IS RECORDED AS
   A SCRATCH,THE ONE WORD ENTRY HAS ONLY THE SIGN BIT SET.
        GIVE EXPECTS TO SEE PASWRD.SYS ON DISK AREA[1,4]. IF
   PASWRD.SYS IS NOT SEEN,GIVE DOES NOT GIVE AN ERROR MESSAGE,BUT
   INSTEAD OMITS THE LISTING OF THE PERSONAL NAME ASSOCIATED WITH
   A PPN. GIVE EXPECTS TO SEE THE RECORD SIZE IN THE RIGHT HALF OF
   THE FIRST WORD IN PASWRD.SYS AND THE VERSION NUMBER IN THE LEFT
   HALF. GIVE EXTRACTS THE PPN AND SIXBIT PERSONAL NAME FROM
   PASWRD.SYS AND BUILDS AN INCORE TABLE WHOSE ENTRY FORMAT IS:
     WORD 0:  XWD PROJECT,PROGRAMMER
     WORD 1-3:SIXBIT /PERSONAL NAME/
   IF THE VERSION IS ZERO,ONLY TWO WORDS ARE GOTTEN FROM PASWRD.SYS
   AND THE THIRD WORD IS MADE ZERO. IF THE VERSION IS NOT ZERO,IT IS
   ASSUMED THAT THE PASSWORD FILE CONTAINS THREE WORDS FOR THE NAME.
3.  DECTAPE - THE DECTAPE TO BE PROCESSED MUST BE MOUNTED ON A
    DECTAPE DRIVE WHOSE LOGICAL NAME IS DTA. GIVE READS THE
    DIRECTORY AND  OTHER DECTAPE BLOCKS IN NON-STANDARD FORMAT.
    HENCE THE JOB RUNNING GIVE MUST HAVE DECTAPE PRIVILEGES(BIT 10).

OUTPUT SPECIFICATIONS
------ --------------
1.  LISTING DEVICE - THE L OR T COMMANDS LISTS A DECTAPE CATATLOG
    ON THE LINE PRINTER OR TELETYPE,RESPECTIVELY. IF THE L COMMAND
    IS USED AND THE LINE PRINTER IS BUSY,GIVE NOTIFIES THE OPERATOR
    "?LIST DEVICE NOT AVALIABLE". THE OPERATOR MAY WRITE THE LISTING
    ON ANOTHER DEVICE (SAY DSK,DTA OR MTA) AND SPOOL THE RESULTING
    FILE LATER BY ASSIGNING THE DEVICE THE LOGICAL NAME LPT. THE
    FILE NAME ON A DIRECTORY DEVICE WILL BE DTAPPN.LST.
2.  DECTAPE - GIVE WRITES THE SPECIFIED SERIAL NUMBER XXXX ONTO THE
    LAST WORD OF BLOCK 100 AS SIXBIT /30XXXX/. THE NUMBER 3 IS THE
    CLASSIFICATION FOR SANDERS DATA FILE CATALOGING SCHEME. THE
    PROJ.-PROG., IF SPECIFIED, IS WRITTEN ONTO THE FIRST WORD OF
    BLOCK 101.


FUNCTIONS OF GIVE COMMANDS
--------- -- ---- --------
         GIVE COMMANDS ONLY REQUEST THE RESOURCES NEEDED TO
    EXECUTE A PARTICULAR FUNCTION. FOR EXAMPLE, THE L COMMAND
    USES THE LPT AND TWO FILES ON THE DISK,BUT DOESN'T NEED A
    DECTAPE ASSIGNMENT.
         THE DATA FILE IS READ AND STORED IN CORE THE FIRST TIME
   A COMMAND REQUESTS THE FILE. IF NO FILE IS FOUND,A NEW DATA FILE
    IS CREATED. EACH TIME A CHANGE IS MADE IN THE DATA FILE,THE FILE
    IS WRITTEN ONTO THE DISK AND GIVEN FILE PROTECTION 455.
1.  C - THE CHANGE COMMAND IS USED TO "OPEN" A DECTAPE FOR
    MODIFICATION OF THE SERIAL NUMBER AND/OR PROJ.-PROG.
    NUMBER. USE OF THIS COMMAND IS SHOWN BELOW(OPERATOR ENTRY
    IS UNDERLINED).
    *C(CARRIAGE RETURN)
     ------------------
    1[2,3] (TAB)   (CARRIAGE RETURN)          NO CHANGE
                   -----------------
    1[2,3] (TAB)  2(CARRIAGE RETURN)          CHANGE SERIAL NUMBER
                  ------------------
    1[2,3] (TAB)  [3,4](CARRIAGE RETURN)      CHANGE PPN
                  ----------------------
    1[2,3] (TAB)  2[3,4](CARRIAGE RETURN)     CHANGE BOTH SERIAL
                  -----------------------     NUMBER AND PPN

         IF NO CHANGE IS GIVEN, THE DATA FILE,DTAPPN.SYS,WILL BE
    UPDATED WITH THE LATEST PPN ON THE DECTAPE. IF ONLY THE SERIAL
    NUMBER IS CHANGED, THE OLD ENTRY IS DELETED AND THE NEW ENTRY
    UPDATED. THE SERIAL NUMBER IS ALSO WRITTEN ONTO THE DECTAPE.
         IF ONLY THE PPN IS CHANGED,THE DECTAPE IS CHECKED TO
    HAVE FILE PROTECTION. IF SO,THE PPN IS WRITTEN ONTO THE
    DECTAPE AND THE DATA FILE. IF THE DECTAPE HAS NO FILE
    PROTECTION,GIVE ASKS:
      "DO YOU WISH TO PROTECT THE TAPE?(TYPE Y OR NO)"
    IF THE ANSWER IS Y AND THE DECTAPE BLOCK 101 IS NOT USED
    BY A FILE,THE SPECIFIED PPN IS WRITTEN ONTO THE FISRT WORD
    OF BLOCK 101. ANY FILES ON THE DECTAPE ARE GIVEN A FILE
    PROTECTION OF 055. IF BLOCK 101 IS ALREADY USED BY A FILE,
    THEN BLOCK 101 WILL FIRST BE TRANSFERRED TO AN AVAILABLE
    BLOCK WITH THE DIRECTORY SLOTS AND FILE LINKAGE POINTERS
    APPROPRIATELY UPDATED.
         IN THE PROCESS OF WRITING NEW INFORMATION BACK ONTO
    THE DECTAPE,GIVE FIRST READS THE TAPE AND CHECKS TO SEE
    IF THE SAME TAPE WAS MOUNTED AS WHEN THE DECTAPE WAS "OPENED".
    IF THE TAPE HAD BEEN CHANGED,GIVE COMPLAINS:
      "A NEW DECTAPE WAS MOUNTED DURING THE C COMMAND
       PLEASE REPEAT THE COMMAND"

2.  S - THE SCRATCH COMMAND WILL ACCEPT AN ARGUMENT OF SERIAL
    NUMBER. IF THE SERIAL NUMBER OF THE DECTAPE IS NOT ZERO,
    IT MUST MATCH THE SPECIFIED ARGUMENT. THE DECTAPE DIRECTORY
    IS CLEARED AND AN ENTRY MADE IN THE DATA FILE SUCH THAT
    GIVE WILL RECOGNIZE THE DECTAPE AS A SCRATCH. THE SERIAL
    NUMBER IS WRITTEN ONTO THE TAPE IF NONE WAS PRESENT.
         IF A CONFLICT IS FOUND BETWEEN THE PPN ON THE DATA
    FILE AND THAT ON THE DECTAPE,GIVE OUTPUTS:
      "?PPN ON DATA FILE AND TAPE DISAGREE
       DECTAPE NOT SCRATCHED"
         IF NO ARGUMENT IS TYPED,A LIST OF THE SCRATCH TAPES
    RECORDED ON THE DATA FILE WILL BE PRINTED ON THE TELETYPE.
3.  P - THREE DIFFERENT ARGUMENTS MAY BE USED WITH THE
    PRINT COMMAND.
    A) P N - PRINT THE PPN'S ASSOCIATED WITH THE SERIAL
    NUMBER N.
    B) P M,N - PRINT THE PPN'S FOR EACH SERIAL NUMBER FROM M 
    TO N INCLUSIVE.
    C) P [PJ,PG] - PRINT ALL THE SERIAL NUMBERS ASSOCIATED WITH
    THE PPN SPECIFIED.
4.  L OR T - LIST OR TYPE THE DECTAPE CATALOG. FIRST, THE SERIAL
    NUMBER,PROJ.-PROG., AND PERSONAL NAME ARE LISTED FOR EACH
    DECTAPE. THEN A CROSS-REFERENCE IS LISTED OF ALL DECTAPES
    ASSOCIATED WITH EACH PROJ.-PROG. FINALLY, ALL SCRATCH
    TAPES ARE LISTED. THE DATE OF THE LISTING IS ALSO GIVEN.

CONFIGURATION
-------------
1.  DTAPPN SIZE - THE DATA FILE HAS A CAPACITY FOR 2048
    DECTAPES. THIS LIMIT MAY BE INCREASED BY REASSEMBLING
    GIVE.MAC WITH THE SYMBOL,FILMIT=^D1024+MORE DECTAPES NEEDED.
2.  PASWRD.SYS VERSION - THE VERSION OF THE SYSTEM PASSWORD
    FILE IS IN THE LEFT HALF OF THE FIRST WORD OF THE
    FILE. IF THE VERSION IS ZERO,TWO WORDS PER RECORD ARE
    ALLOCATED FOR THE PERSONAL NAME. IF THE VERSION IS NOT
    ZERO,THREE WORDS ARE USED.
3.  GIVE LOCATION - USUALLY GIVE IS RUN FROM DISK AREA[1,4]
    WHERE THE PASSWORD AND DATA FILES ARE STORED. GIVE
    MAY BE RUN UNDER A DIFFERENT PROJ.-PROG. NUMBER PROVIDED
    THE JOB HAS INFINITE DISK READ/WRITE PRIVILEGES(BIT 10)
    TO ACCESS PASWRD.SYS AND DTAPPN.SYS ON AREA[1,4].


PREPARATION
-----------
1.  ASSEMBLING WITH SOURCE GIVE.MAC ON DISK:
        R MACRO
        *GIVE,_GIVE
2. LOADING:
        R LOADER
        *GIVE(ALTMODE)
3. STORAGE ON DISK:
        SAVE DSK GIVE
4. EXECUTION:
        RUN DSK GIVE
        *



* * * END OF GIVE DOCUMENTATION * * *