UMOUNT.DOC--CHANGES FROM VERSION 17 TO 20(10)
OCTOBER, 1971

COPYRIGHT 1971, DIGITAL EQUIPMENT CORP., MAYNARD, MASS.

1.	SUMMARY

	THE NEW FORMAT FOR THE VERSION NUMBER IS USED.
THE SLEEP UUO HAS BEEN REPLACED WITH HIBERNATE/WAKE UUOS FOR
SYNCHRONIZATION WITH OMOUNT.  UMOUNT INFORMS THE USER IF THERE
IS NO OMOUNT RUNNING WHICH CAN SERVICE THIS REQUEST.

2.	EXTERNAL CHANGES

	IF, WHEN AN OPERATOR REQUEST IS QUEUED, THERE IS NO OMOUNT
RUNNING WHICH CAN SERVICE THE REQUEST, THE FOLLOWING IS TYPED:

	NO OPR. JOB FOR THIS REQUEST

THE REQUEST IS QUEUED IN ANY CASE (UNLESS THE /PAUSE SWITCH WAS GIVEN).

3.	KNOWN DEFICIENCIES

	(1)  ONE CANNOT TYPE AHEAD WHEN UMOUNT (FILE W, MOUNT, & DISMOUNT
	COMMANDS) IS WAITING FOR THE REQUEST TO BE PROCESSED.
	THE REASON IS THAT UMOUNT RUNS WITH THE PRIVILEGE BIT
	JACCT=1 WHICH SUPPRESSES RETURN TO MONITOR LEVEL ON ^C AND
	THEREFORE UMOUNT MUST READ ALL TYPIN ITSELF IN ORDER TO EXIT
	IF A ^C IS TYPED.
	THIS WAIT STATE IS ALWAYS PRECEEDED WITH THE MESSAGE:
	'WAITING...'

	(2)  ON DISMOUNT OF NON-FILE STRUCTURES, THE DEASSIGN IS DONE BY
	UMOUNT AFTER ITS REQUEST TO THE OPERATOR IS SATISFIED.
	THEREFORE THE DEVICE WILL NOT BE DEASSIGNED BY THE DISMOUNT
	COMMAND IF THE USER INTERRUPTS THE WAIT WITH ^C.

	(3)  ON MOUNT OF NON-FILE STRUCTURES, IF THE DEVICE NAME IS GENERIC
	AND NO LOGICAL NAME IS SPECIFIED, UMOUNT CANNOT KNOW WHICH
	SPECIFIC DRIVE THE OPERATOR CHOSE. THEREFORE, IN THIS
	CASE, THE CONFIRMING MESSAGE MAY BE INCORRECT OR UNINFORMATIVE.
	ITS A GOOD IDEA TO ALWAYS WORK WITH A LOGICAL NAME.

4.	INSTALLATION REQUIREMENTS

UMOUNT VERSION 20 REQUIRES OMOUNT VERSION 22.

5.	INTERNAL CHANGES

	UMOUNT AND OMOUNT NOW SYNCHRONIZE WITH EACH OTHER VIA
HIBERNATE AND WAKE UUOS.  IN ORDER THAT OMOUNTS MAY BE RUN
SELECTIVELY FOR 'FILE' AND/OR 'MOUNT-DISMOUNT' REQUESTS,
THE FOLLOWING TAKES PLACE:

	(1)  OMOUNT RUNS UNDER ONE OF THE FOLLOWING NAMES DEPENDING
	UPON WHICH REQUESTS IT IS TO SERVICE:

	OPROMO - ALL REQUESTS (FILE & MOUNT-DISMOUNT)
	OPRMNT - ONLY MOUNT-DISMOUNT REQUESTS
	OPRPLS - PLEASE ONLY
	OPRFIL - ONLY FILE REQUESTS
	OMOUNT - NO REQUESTS (ONLY OPERATOR COMMANDS)

	(2)  WHEN UMOUNT QUEUES A REQUEST TO OMOUNT, IT
	LOOKS TO SEE IF THERE IS CURRENTLY RUNNING AN OMOUNT OF THE
	'PROPER' NAME.  IF ONE OR MORE ARE FOUND THEY ARE WAKENED
	AND UMOUNT HIBERNATES.

	(3)  IF NO APPROPRIATE OMOUNT IS FOUND, THE USER IS INFORMED
	AND THE REQUEST IS QUEUED ANYWAY (UNLESS /PAUSE).

	(4)  WHEN OMOUNT HAS SERVICED THE REQUEST IT WAKES THE UMOUNT
	JOB.